## Slide 1: Mass Storage Structure

## Slide 2: Hard Disk Structure

## Slide 3: Key concepts
Disk Arm: The heads are attached to a disk arm that moves all the heads as a unit.
Arm assembly : Has multiple disk arms.
Platter: Each disk platter has a flat circular shape, like a CD. The two surfaces of a platter are covered with a magnetic material. We store information by recording it magnetically on the platters.
Track: The surface of a platter is logically divided into circular tracks
Sector: Each Track is subdivided into sectors.
Cylinder: The set of tracks that are at one arm position makes up a cylinder.
Spindle Rod: Is the rod in middle which moves the platters.
Transfer rate: The transfer rate is the rate at which data flow between the drive and the computer.
Positioning Time: Consists of two parts: the time necessary to move the disk arm to the desired cylinder, called the seek time, and the time necessary for the desired sector to rotate to the disk head, called the rotational latency.
Head Crash: Although the disk platters are coated with a thin protective layer, the head will sometimes damage the magnetic surface called Head crash.
Effective transfer rates: The transfer rate may be the rate at which bits can be read from the magnetic media by the disk head, but that is different from the rate at which blocks are delivered to the operating system.

## Slide 4: Connection to Computer
A disk drive is attached to a computer by a set of wires called an I/O bus
Controllers: The data transfers on a bus are carried out by special electronic processors called controllers
Host Controller: The host controller is the controller at the computer end of the bus.
Disk Controller: A disk controller is built into each disk drive.
The host controller then sends the command via messages to the disk controller.
Disk controller operates the disk-drive hardware to carry out the command.
Disk controllers usually have a built-in cache. Data transfer at the disk drive happens between the cache and the disk surface
Data transfer to the host, at fast electronic speeds, occurs between the cache and the host controller.

## Slide 5: Solid State Disks
SSD is nonvolatile memory that is used like a hard drive.
There are many variations of this technology, from DRAM with a battery to allow it to maintain its state in a power failure.
SSDs have the same characteristics as traditional hard disks but can be more reliable because they have no moving parts and faster because they have no seek time or latency.
Consume less power.
Some SSDs are designed to connect directly to the system bus

## Slide 6: Magnetic Tapes
Magnetic tape was used as an early secondary-storage medium.
Its access time is slow compared with that of main memory and magnetic disk.
Random access to magnetic tape is about a thousand times slower than random access to magnetic disk.
Tapes are used mainly for backup, for storage of infrequently used information, and as a medium for transferring information from one system to another.
A tape is kept in a spool and is wound or rewound past a read–write head. Moving to the correct spot on a tape can take minutes, but once positioned, tape drives can write data at speeds comparable to disk drives.

## Slide 7: Disk Structure
Logical Blocks: Modern magnetic disk drives are addressed as large one-dimensional arrays of logical blocks.
The size of a logical block is usually 512 bytes, although some disks can be low-level formatted to have a different logical block size, such as 1,024 bytes.
The one-dimensional array of logical blocks is mapped onto the sectors of the disk sequentially.
Sector 0 is the first sector of the first track on the outermost cylinder.
The mapping proceeds in order through that track
Then through the rest of the tracks in that cylinder.
And then through the rest of the cylinders from outermost to innermost.
Logical address can be converted to a cylinder number, a track number within that cylinder, and a sector number within that track.

## Slide 8: Disk Structure
Most disks have some defective sectors, but the mapping hides this by substituting spare sectors from elsewhere on the disk.
The number of sectors per track is not a constant on some drives.
Outer tracks can hold more sectors
As we move from outer zones to inner zones, the number of sectors per track decreases
The drive increases its rotation speed as the head moves from the outer to the inner tracks to keep the same rate of data moving under the head.
The density of bits decreases from inner tracks to outer tracks to keep the data rate constant.
This method is used in hard disks and is known as constant angular velocity (CAV).
The outer zone of a disk usually has several hundred sectors per track.
Large disks have tens of thousands of cylinders.

## Slide 9: Host attached Storage
Host-attached storage is storage accessed through local I/O ports.
Typical desktop PC uses an I/O bus architecture called IDE or ATA
This architecture supports a maximum of two drives per I/O bus.
High-end workstations and servers generally use more sophisticated I/O architectures such as fiber channel (FC).
FC is high-speed serial architecture that can operate over optical fiber or over a four-conductor copper cable.

## Slide 10: Network attached storage
A network-attached storage (NAS) device is a special-purpose storage system that is accessed remotely over a data network.
Clients access network-attached storage via a remote-procedure-call interface.
The remote procedure calls (RPCs) are carried via TCP or UDP over an IP network usually over LAN.
The network attached storage unit is usually implemented as a RAID array with software that implements the RPC interface.

## Slide 11: Storage Area Network
Storage I/O operations consume bandwidth on the data network, thereby increasing the latency of network communication.
A storage-area network (SAN) is a private network using storage protocols rather than networking protocols.
Multiple hosts and multiple storage arrays can attach to the same SAN, and storage can be dynamically allocated to hosts.
A SAN switch allows or prohibits access between the hosts and the storage.

## Slide 12: Disk Scheduling
The access time has two major components, seek time and rotational latency.
The disk bandwidth is the total number of bytes transferred, divided by the total time between the first request for service and the completion of the last transfer
Whenever a process needs I/O to or from the disk, it issues a system call to the operating system.
  Whether this operation is input or output
  What the disk address for the transfer is
  What the memory address for the transfer is
  What the number of sectors to be transferred is
If the desired disk drive and controller are available, the request can be serviced immediately.
If the drive or controller is busy, any new requests for service will be placed in the queue of pending requests

## Slide 13: First come first Serve Scheduling
queue 98, 183, 37, 122, 14, 124, 65, 67
head starts at 53

## Slide 14: Shortest Seek Time First Scheduling
The SSTF algorithm selects the request with the least seek time from the current head position.
queue 98, 183, 37, 122, 14, 124, 65, 67
head starts at 53

## Slide 15: SCAN Scheduling
The disk arm starts at one end of the disk and moves toward the other end, servicing requests as it reaches each cylinder, until it gets to the other end of the disk.
At the other end, the direction of head movement is reversed, and servicing continues.
The SCAN algorithm is sometimes called the elevator algorithm.

## Slide 16: C-SCAN Scheduling
Circular SCAN (C-SCAN) scheduling is a variant of SCAN designed to provide a more uniform wait time.
When the head reaches the other end, however, it immediately returns to the beginning of the disk without servicing any requests on the return trip.
The C-SCAN scheduling algorithm essentially treats the cylinders as a circular list that wraps around from the final cylinder to the first one.
Modification is LOOK scheduling

## Slide 17: Disk Formatting
Before a disk can store data, it must be divided into sectors that the disk controller can read and write. This process is called low-level formatting, or physical formatting.
Low-level formatting fills the disk with a special data structure for each sector.
The data structure for a sector typically consists of a header, a data area (usually 512 bytes in size), and a trailer.
The header and trailer contain information used by the disk controller, such as a sector number and an error-correcting code (ECC).
When the controller writes a sector of data during normal I/O, the ECC is updated with a value calculated from all the bytes in the data area.
When the sector is read, the ECC is recalculated and compared with the stored value. If there is a mismatch then the sector is corrupted.
If enough bits have not been corrupted then ECC reports a recoverable soft error. The controller automatically does the ECC processing whenever a sector is read or written.

## Slide 18: Disk Formatting
While disk formatting disk controller can choose the size of data block. Generally the sizes are 256, 516, 1024 bytes.
Formatting a disk with a larger sector size means that fewer sectors can fit on each track; but it also means that fewer headers and trailers are written on each track and more space is available for user data.
Before it can use a disk to hold files, the operating system still needs to record its own data structures on the disk.
Partition: OS Partitions the disks into one or more group of cylinders.
The operating system can treat each partition as though it were a separate disk.
Logical formatting: The operating system stores the initial file-system data structures onto the disk. These data structures may include maps of free and allocated space and an initial empty directory.
Most file systems group blocks together into larger chunks, frequently called clusters.
Raw disk: Some operating systems give special programs the ability to use a disk partition as a large sequential array of logical blocks, without any file-system data structures.
Raw I/O bypasses all the file-system services, such as the buffer cache, file locking, prefetching, space allocation, file names, and directories.

## Slide 19: Boot Block:
When Computer is powered up or rebooted, it must have an initial program to run. Initial program is called Bootstrap program.
It initializes all aspects of the system, from CPU registers to device controllers and the contents of main memory, and then starts the operating system
Bootstrap program finds the operating-system kernel on disk, loads that kernel into memory, and jumps to an initial address to begin the operating-system execution.
Mostly bootstrap is stored in Read only memory (ROM).
The problem is that changing this bootstrap code requires changing the ROM hardware chips.
For this reason, most systems store a tiny bootstrap loader program in the boot ROM whose only job is to bring in a full bootstrap program from disk.

## Slide 20: Boot Block
The full bootstrap program can be changed easily: a new version is simply written onto the disk.
The full bootstrap program is stored in the “boot blocks” at a fixed location on the disk.
A disk that has a boot partition is called a boot disk or system disk.
The code in the boot ROM instructs the disk controller to read the boot blocks into memory.
Full bootstrap program is able to load the entire operating system from a non-fixed location on disk.
Boot partition—contains the operating system and device drivers.
The Windows system places its boot code in the first sector on the hard disk, which it terms the master boot record, or MBR.
Booting begins by running code that is resident in the system’s ROM memory. This code directs the system to read the boot code from the MBR.
Once the system identifies the boot partition, it reads the first sector from that partition

## Slide 21: Bad Blocks
Scan the disk to find bad blocks while the disk is being formatted.
Any bad blocks that are discovered are flagged as unusable so that the file system does not allocate them.
Data that resided on the bad blocks usually are lost.
The controller maintains a list of bad blocks on the disk.
The list is initialized during the low-level formatting at the factory and is updated over the life of the disk.
Low-level formatting also sets aside spare sectors not visible to the operating system.

## Slide 22: Sector Sparing
The controller can be told to replace each bad sector logically with one of the spare sectors. This scheme is known as sector sparing or forwarding.
A typical bad-sector transaction might be as follows:
  The operating system tries to read logical block 87.
  The controller calculates the ECC and finds that the sector is bad. It reports this finding to the operating system.
  The next time the system is rebooted, a special command is run to tell the controller to replace the bad sector with a spare.
  After that, whenever the system requests logical block 87, the request is translated into the replacement sector’s address by the controller.

## Slide 23: Sector Slipping
Such a redirection by the controller could invalidate any optimization by the operating system’s disk-scheduling algorithm
most disks are formatted to provide a few spare sectors in each cylinder and a spare cylinder as well.
When a bad block is remapped, the controller uses a spare sector from the same cylinder, if possible
some controllers can be instructed to replace a bad block by sector slipping.
Suppose that logical block 17 becomes defective and the first available spare follows sector 202.
Sector slipping then remaps all the sectors from 17 to 202, moving them all down one spot.
Slipping the sectors in this way frees up the space of sector 18 so that sector 17 can be mapped to it

## Slide 24: Swap Space Management
Systems that implement swapping may use swap space to hold an entire process image, including the code and data segments.
Paging systems may simply store pages that have been pushed out of main memory.
The amount of swap space needed on a system can therefore vary from a few megabytes of disk space to gigabytes,
It may be safer to overestimate than to underestimate the amount of swap space required.
Swap Space can be carved out of the normal file system, or it can be in a separate disk partition.
If the swap space is simply a large file within the file system, normal file-system routines can be used to create it, name it, and allocate its space. This is inefficient.
Alternatively, swap space can be created in a separate raw partition. No file system or directory structure is placed in this space.
A separate swap-space storage manager is used to allocate and deallocate the blocks from the raw partition.

## Slide 25: Swap Area
A swap area may be in either a swap file on a regular file system or a dedicated swap partition
Each swap area consists of a series of 4-KB page slots, which are used to hold swapped pages.
Associated with each swap area is a swap map—an array of integer counters.
If the value of a counter is 0, the corresponding page slot is available.
The value of the counter indicates the number of mappings to the swapped page. For example, a value of 3 indicates that the swapped page is mapped to three different processes

## Slide 26: RAID: Redundant Arrays of Independent Disks
Since disks are prone to failures we need to store data redundantly to increase reliability.
Mirroring: The simplest (but most expensive) approach to introducing redundancy is to duplicate every disk.
With mirroring, a logical disk consists of two physical disks, and every write is carried out on both disks. The result is called a mirrored volume.
If one of the disks in the volume fails, the data can be read from the other.
Data will be lost only if the second disk fails before the first failed disk is replaced.
Mean time to repair: The time it takes (on average) to replace a failed disk and to restore the data on it.
Power failures are a particular source of concern, if writes are in progress to the same block in both disks, and power fails before both blocks are fully written, the two blocks can be in an inconsistent state.
One solution to this problem is to write one copy first, then write to next disk.
Another is to add a solid-state nonvolatile RAM (NVRAM) cache to the RAID array. This write-back cache is protected from data loss during power failures, so the write can be considered complete at that point.

## Slide 27: Improvement in Performance via Parallelism
With disk mirroring, the rate at which read requests can be handled is doubled, since read requests can be sent to either disk.
With multiple disks, we can improve the transfer rate as well by striping data across the disks.
In its simplest form, data striping consists of splitting the bits of each byte across multiple disks; such striping is called bit-level striping.
if we have an array of eight disks, we write bit i of each byte to disk I
Bit-level striping can be generalized to include a number of disks that either is a multiple of 8 or divides 8.
Block-level striping: Blocks of a file are striped across multiple disks; with n disks, block i of a file goes to disk (i mod n) + 1.

## Slide 28: RAID Levels:
Striping provides high data-transfer rates, but it does not improve reliability.
Schemes provide redundancy at lower cost by using disk striping combined with “parity” bits
There are different RAID levels which have different cost–performance trade-offs.

## Slide 29: RAID Level 0
RAID level 0 refers to disk arrays with striping at the level of blocks but without any redundancy (such as mirroring or parity bits)
RAID level 0 is used in high-performance applications where data loss is not critical.

## Slide 30: RAID Level 1
RAID level 1 refers to disk mirroring. Figure 10.11(b) shows a mirrored organization.
Rebuilding is easiest for RAID level 1, since data can be copied from another disk.
RAID level 1 is popular for applications that require high reliability with fast recovery

## Slide 31: RAID Level 2
Also Known as Memory-style error-correcting code (ECC) organization.
Each byte in a memory system may have a parity bit associated with it that records whether the number of bits in the byte set to 1 is even (parity = 0) or odd (parity = 1).
If one of the bits in the byte is damaged (either a 1 becomes a 0, or a 0 becomes a 1), the parity of the byte changes and thus does not match the stored parity.
Thus, all single-bit errors are detected by the memory system.
Error-correcting schemes store two or more extra bits and can reconstruct the data if a single bit is damaged.
First bit of each byte can be stored in disk 1, the second bit in disk 2, and so on. The error-correction bits are stored in further disks.
If one of the disks fails, the remaining bits of the byte and the associated error-correction bits can be read from other disks and used to reconstruct the damaged data.
RAID level 2 requires only three disks’ overhead for four disks of data.

## Slide 32: RAID Level 3
Also called bit-interleaved parity organization.
Disk controllers can detect whether a sector has been read correctly, so a single parity bit can be used for error correction as well as for detection
we can figure out whether any bit in the sector is a 1 or a 0 by computing the parity of the corresponding bits from sectors in the other disks.
RAID level 3 has two advantages over level 1, the storage overhead is reduced because only one parity disk is needed for several regular disks and since reads and writes of a byte are spread out over multiple disks with N-way striping of data, the transfer rate for reading or writing a single block is N times as fast as with RAID level 1.
Problem is and with all parity based RAID levels—is the expense of computing and writing the parity.
Many RAID storage arrays include a hardware controller with dedicated parity hardware.

## Slide 33: RAID Level 4
Also called block-interleaved parity organization, uses block-level striping, as in RAID 0, and in addition keeps a parity block on a separate disk for corresponding blocks from N other disks.
If one of the disks fails, the parity block can be used with the corresponding blocks from the other disks to restore the blocks of the failed disk.
The transfer rates for large reads are high, since all the disks can be read in parallel. Large writes also have high transfer rates, since the data and parity can be written in parallel.

## Slide 34: RAID Level 5
Also called block-interleaved distributed parity, differs from level 4 in that it spreads data and parity among all N+1 disks, rather than storing data in N disks and parity in one disk.
For each block, one of the disks stores the parity and the others store data.
With an array of five disks, the parity for the nth block is stored in disk (n mod 5)+1.
A parity block cannot store parity for blocks in the same disk, because a disk failure would result in loss of data as well as of parity.
RAID 5 is the most common parity RAID system.

## Slide 35: RAID Level 6
Also called the P + Q redundancy scheme, is much like RAID level 5 but stores extra redundant information to guard against multiple disk failures.
Instead of parity, error-correcting codes such as the Reed–Solomon codes are used.
2 bits of redundant data are stored for every 4 bits of data— compared with 1 parity bit in level 5—and the system can tolerate two disk failures.

## Slide 36: RAID levels 0 + 1 and 1 + 0
RAID level 0 + 1 refers to a combination of RAID levels 0 and 1. RAID 0 provides the performance, while RAID 1 provides the reliability.
Common in environments where both performance and reliability are important.
In RAID 0 + 1, a set of disks are striped, and then the stripe is mirrored to another, equivalent stripe

## Slide 37: Snapshot and Replication
A snapshot is a view of the file system before the last update took place.
Replication involves the automatic duplication of writes between separate sites for redundancy and disaster recovery.
Replication can be synchronous or asynchronous.
In synchronous replication, each block must be written locally and remotely before the write is considered complete.
whereas in asynchronous replication, the writes are grouped together and written periodically.
Asynchronous replication can result in data loss if the primary site fails, but it is faster and has no distance limitations.
One other aspect of most RAID implementations is a hot spare disk or disks.
A hot spare is not used for data but is configured to be used as a replacement in case of disk failure.
A hot spare can be used to rebuild a mirrored pair should one of the disks in the pair fail. In this way, the RAID level can be reestablished automatically, without waiting for the failed disk to be replaced.
Allocating more than one hot spare allows more than one failure to be repaired without human intervention.

## Slide 38: Problems with RAID
RAID does not always assure that data are available for the operating system and its users.
Incomplete writes, if not properly recovered, could result in corrupt data.
Some other process could accidentally write over a file system’s structures, too.
RAID protects against physical media errors, but not other hardware and software errors.

## Slide 39: Checksums
Checksums: Solaris ZFS file system takes an innovative approach to solving these problems through the use of checksums.
ZFS maintains internal checksums of all blocks, including data and metadata.
These checksums are not kept with the block that is being checksummed. Rather, they are stored with the pointer to that block.

## Slide 40: Pool Storage System
issue with most RAID implementations is lack of flexibility.
what if one file system is too large to fit on a five-disk RAID level 5 set.
In ZFS Disks, or partitions of disks, are gathered together via RAID sets into pools of storage.
A pool can hold one or more ZFS file systems. The entire pool’s free space is available to all file systems within that pool.

## Slide 41: Stable Storage Implementation
A disk write results in one of three outcomes:
  Successful completion. The data were written correctly on disk.
  Partial failure.
  Total failure.
Output operation is executed as follows:
  Write the information onto the first physical block.
  When the first write completes successfully, write the same information onto the second physical block.
  Declare the operation complete only after the second write completes successfully.
If one block contains a detectable error then we replace its contents with the value of the other block. If neither block contains a detectable error, but the blocks differ in content, then we replace the content of the first block with that of the second.
Many storage arrays add NVRAM as a cache. Since the memory is nonvolatile, it can be trusted to store the data en route to the disks.